## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Group 1, variant 1
Developement of a 3D environment sampling device
Beatrice Pedretti, Mauro di Liddo, Davide Goshen

## Slide 2: Aim of the project
Di Liddo, Goshen, Pedretti
2

## Slide 3: Requirements: hardware
MG996R
HCSR04
Wooden case
Connection elements
& breadbord
High-Torque digital servo motors:
Stall torque: 10 kg
Movement range: 180°
Operating voltage: 4.8 V a 7.2 V
Running Current 500 mA – 900 mA (6 V)
Weight: 55 g
Cypress CY8CKIT-059
Di Liddo, Goshen, Pedretti
3

## Slide 4: Requirements: hardware
MG996R
HC SR04
Wooden case
Connection elements
& breadbord
Ultrasonic ranging module:
Measured distance range: 2 cm – 400 cm
Working voltage: DC 5 V
Working current: 15 mA
Working frequency: 40 Hz
Measuring angle: 15°
Cypress CY8CKIT-059
Di Liddo, Goshen, Pedretti
4

## Slide 5: Requirements: hardware
MG996R
HCSR04
Connection elements
& breadbord
Wooden case
Cypress CY8CKIT-059
Di Liddo, Goshen, Pedretti
Breadboard
Jumper wires
Handmade aluminium support
Metal supports
Copper wire for electrical insulation
5

## Slide 6: Requirements: hardware
MG996R
HCSR04
Connection elements
& breadbord
Wooden case
Cypress CY8CKIT-059
Wiring configuration
Di Liddo, Goshen, Pedretti
6

## Slide 7: Requirements: hardware
MG996R
HCSR04
Wooden case
Cypress CY8CKIT-059
Connection elements
& breadbord
Di Liddo, Goshen, Pedretti
7

## Slide 8: Requirements: hardware
MG996R
HCSR04
Wooden case
Cypress CY8CKIT-059
Connection elements
& breadbord
Di Liddo, Goshen, Pedretti
8

## Slide 9: Requirements: hardware
MG996R
HCSR04
Wooden case
Cypress CY8CKIT-059
Connection elements
& breadbord
Di Liddo, Goshen, Pedretti
9

## Slide 10: Requirements: software
Visual Studio Code
PSoC Creator
MATLAB 2017b with Computer Vision Toolbox
Kivy
Di Liddo, Goshen, Pedretti
10

## Slide 11: Requirements: software
PSoC Creator
Visual Studio Code
MATLAB 2017b with Computer Vision Toolbox
Kivy
Di Liddo, Goshen, Pedretti
11

## Slide 12: Requirements: software
PSoC Creator
IDE
Visual Studio Code
MATLAB 2017b with Computer Vision Toolbox
Kivy
Di Liddo, Goshen, Pedretti
12

## Slide 13: Requirements: software
PSoC Creator
Visual Studio Code
MATLAB 2017b with Computer Vision Toolbox
Kivy
Di Liddo, Goshen, Pedretti
13

## Slide 14: Calibration
First servomotor:
0 angle: lies on the positive portion of the X-axis
90 angle: lies on the positive portion of the Y-axis
180 angle: lies on the negative portion of the X-axis
Second servomotor:
0 angle: 60° angle between the Z-axis and the straight line which is the extension of the arm to which the sonar is linked.
90 angle: 0 angle + 90° = 150° (almost)
Di Liddo, Goshen, Pedretti
14

## Slide 15: Calibration
alpha = SERVO_MID_ANGLE - Servo_GetPosition1()
beta = Servo_GetPosition2() + ANGLE_ZERO-SERVO_MID_ANGLE
SERVO_MID_ANGLE = 90
ANGLE_ZERO = 60
Di Liddo, Goshen, Pedretti
15

## Slide 16: Coordinates computation
D2
ARM_LENGTH
Z1
D2: distance between the middle of the crankshaft of the second servomotor and the Z-axis
ARM_LENGTH: length of the connection component that allows the rotation of the sonar solidally with the second crankshaft
pos_servo1_rad: alpha in rad
pos_servo2_rad: beta in rad
pos_servo2_z_rad: beta + ANGLE_ZERO (rad)
Z1 is the height of the crankshaft of the second servomotor
Di Liddo, Goshen, Pedretti
16

## Slide 17: Coordinates computation
D2
ARM_LENGTH
Z1
X = (D2 + (ARM_LENGTH + distance_real) * cos(pos_servo2_rad)) * sin(pos_servo1_rad); Y = (D2 + (ARM_LENGTH + distance_real) * cos(pos_servo2_rad)) * cos(pos_servo1_rad); Z = Z1 - (ARM_LENGTH + distance_real) * cos(pos_servo2_z_rad);
Di Liddo, Goshen, Pedretti
17

## Slide 18: Finite-states machine
Di Liddo, Goshen, Pedretti
18

## Slide 19: Finite-states machine
Di Liddo, Goshen, Pedretti
19

## Slide 20: State: IDLE
Wait for start
(if first connection, start components)
Modify angular steps:
- 5° (default)
- 10°
Reset variables
Di Liddo, Goshen, Pedretti
20

## Slide 21: Finite-states machine
Di Liddo, Goshen, Pedretti
21

## Slide 22: State: SCAN
Sweep of kinematic chain with one for cycle, switching directions and rising the scanner
2
For every step of the chain, check if returned servo angle is correct
3
If yes, compute coordinates (with limitations)
4
If the object is removed mid sweep, display reconstructed image immediately
5
Else, wait until scan is complete and then go to display
Di Liddo, Goshen, Pedretti
22

## Slide 23: Finite-states machine
Di Liddo, Goshen, Pedretti
23

## Slide 24: State: DISPLAY
Mainly performed in the GUI
Pop-up windows: point cloud and ballpoint mesh
On pression of ‘P’ key, a screenshot of the mesh is captured
24

## Slide 25: GUI
Python language and Kivy framework
UltraSound Sensor for
EnvironmeNT Recording and Point-cloud Reconstruction Integrated Scanning Equipment
Di Liddo, Goshen, Pedretti
25

## Slide 26: GUI
Connect/Disconnect button:
it sends the ‘v’ and ‘d’ letters over UART. PSoC is programmed to respond with a specific string, it allows automatical connection/disconnection
Python language and Kivy framework
Di Liddo, Goshen, Pedretti
26

## Slide 27: GUI
Step angle
The user has the chance to change the angle step to:
5 degrees by pushing 5 (higher quality image)
10 degrees by pushing 10 (lower quality image)
Python language and Kivy framework
Di Liddo, Goshen, Pedretti
27

## Slide 28: GUI
Start & Stop buttons
It sends over UART respectively ‘b’ and ‘s’. PSoC will recognize those letter and will manage the states progression.
Python language and Kivy framework
Di Liddo, Goshen, Pedretti
28

## Slide 29: GUI
Display button
It starts the reconstruction of the image through a point cloud and a ballpoint algorithm
Python language and Kivy framework
Di Liddo, Goshen, Pedretti
29

## Slide 30: Python framework
Di Liddo, Goshen, Pedretti
30

## Slide 31: Python framework
Graphic User Interface classes, managing visual elements on the screen
Di Liddo, Goshen, Pedretti
31

## Slide 32: Python framework
Used by Kivy framework to create a program whose graphic representation is in GUI.kv file
Hierarchical description of the various windows
Di Liddo, Goshen, Pedretti
32

## Slide 33: Python framework
Main GUI window:
__init__
on_press buttons: «binding» between element and event (NB. use separate threads)
  connectionProcess
  step_setter
  startProcess
  stopProcess
Di Liddo, Goshen, Pedretti
33

## Slide 34: Python framework
Wrapper for open3d framework in easier interface
Takes as input a 3 columns vector; each row is a point read by numpy with np.loadtxt(file).
ballpoint
cloud_output, ballpoint_output_png, ballpoint_write
cloud_visualize, ballpoint_visualize
Di Liddo, Goshen, Pedretti
34

## Slide 35: Image reconstruction
XYZ over UART
Di Liddo, Goshen, Pedretti
35

## Slide 36: Image reconstruction
XYZ coordinates saved into .xyz file
Di Liddo, Goshen, Pedretti
36

## Slide 37: Image reconstruction
XYZ coordinates saved into .xyz file
Di Liddo, Goshen, Pedretti
37

## Slide 38: Image reconstruction
3D Points cloud
Di Liddo, Goshen, Pedretti
38

## Slide 39: Image reconstruction
3D mesher
Di Liddo, Goshen, Pedretti
39

## Slide 40: Conclusions: distance suggestion & limits
Unsufficient distance
Di Liddo, Goshen, Pedretti
40

## Slide 41: Conclusions: distance suggestion & limits
Sufficient distance
Di Liddo, Goshen, Pedretti
41

## Slide 42: Conclusions: distance suggestion & limits
Sufficient distance
In order to decrease the undected portion we have to increase the distance
Di Liddo, Goshen, Pedretti
42

## Slide 43: Conclusions: distance suggestion & limits
Sufficient distance
In order to decrease the undected portion we have to increase the distance
Di Liddo, Goshen, Pedretti
Too high distance usually give us outliers
43

## Slide 44: Conclusions: distance suggestion & limits
Compromised distance: ~ 20 - 25 cm
Di Liddo, Goshen, Pedretti
Compromised dimensions
44

## Slide 45: Conclusions: limits
Distance and dimensions requirements in order to avoid outliers
Servo’s resolution: 1.2°
lowest integer step angle must be 2°
 less points detected
Sonar returns correct distances only for points on planes parallel or almost parallel to it
Di Liddo, Goshen, Pedretti
Just one sonar to reconstruct an image.
45

## Slide 46: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Thank you for your attention